## Slide 1: Body Schema in Robotics: A Review
Authors: Matej Hoffmann, Hugo Gravato Marques, Alejandro Hernandez Arieta, Hidenobu Sumioka, Max Lungarella, and Rolf Pfeifer
Presenter: Ruohua Li

## Slide 2: Outline
Body representations in biology
Body representations in robotics
Body representations in robotics →biology

## Slide 3: In Biology
Definitions in biology (disorders → definitions)
Plasticity
Coordinate transformations
Forward model

## Slide 4: Definitions & Differentiations
Functional axis – action vs perception
  Body schema: sensorimotor representation for movements/actions
  Body image: body structural description & body semantics
Grounding – two streams in visual nervous system
Disorders – proof for differentiation

## Slide 5: Two Streams in Visual Nervous System
Dorsal vs ventral pathways

## Slide 6: Plasticity
Plasticity in development
  Visual–proprioceptive calibration: body ownership & agency
Plasticity in short time
  Fluid body image: rubber hand illusion
Plasticity in tool use
  Extendable body schema: peripersonal space

## Slide 7: Coordinate Transformation
Spatial sensing
  LIP (lateral intraparietal area), VIP (ventral intraparietal area), premotor areas, PRR (parietal reach region), & anterior parietal area
Parallel transformation
  Gain encoding & gain modulation

## Slide 8: Gain Encoding & Gain Modulation

## Slide 9: Gain Encoding & Gain Modulation
or

## Slide 10: Similarities – Cross Attention
or

## Slide 11: Forward Model

## Slide 12: In Robotics
Necessity
Explicit model
Implicit model

## Slide 13: Pros vs Cons
Pros
  Required for precise control
  Required for state estimation
Cons
  Considerable costs for development
  Inability to bear changeable conditions

## Slide 14: Explicit Models
Fixed kinematic models
  Rigid body kinematics only
  Not adaptive
Self-calibration of kinematic models
  Only possible when system receives info from more than one source
  Preferably to be incremental & online

## Slide 15: Self-Calibration
Online learning of kinematic parameters

## Slide 16: Explicit Models
Automatic Model Synthesis
  Robotic manipulator can synthesize and adapt its kinematic model from self-observation
  Hyperparameters like the number of joints and body parts are prior knowledge
  The signals from the robots’ own sensors are used to validate the model
  There is a population of candidate models involved

## Slide 17: Automatic Model Synthesis
Online learning of kinematic parameters

## Slide 18: Implicit Models
Take forms of an NN or look-up table
  Provide mappings mainly in parameters
  Can handle non-linearities
Self-recognition
  Learn to separate signals from its own body with counterparts from the environment
  Takes advantages of invariances & correlations in sensorimotor perceptions
    Visual input → motor input
    Arms fixed in vision
    Hands moves periodically in vision

## Slide 19: Neural Network for Representations
MLP for inverse kinematics approximation

## Slide 20: Robots as Models of Biological Representation
Nonaction-oriented body representation
  Body image
  Explore body representation when multi-modal signals are available
Action-oriented body representation
  Body schema
  Explore body representation changes when actions are in motion

## Slide 21: Cross-modal Body Representations w/ Attention

## Slide 22: Multi-Modal Map Correlations for SSL
Audio & vision co-train for SSL

## Slide 23: References
M. Hoffmann, H. Marques, A. Arieta, H. Sumioka, M. Lungarella and R. Pfeifer, "Body Schema in Robotics: A Review," in IEEE Transactions on Autonomous Mental Development, vol. 2, no. 4, pp. 304-324, Dec. 2010, doi: 10.1109/TAMD.2010.2086454.
A. Pouget, S. Deneve, and J.-R. Duhamel, “A computational perspective on the neural basis of multisensory spatial representations,” Nature Rev. Neurosci., vol. 3, pp. 741–747, 2002.
M. Hikita, S. Fuke, M. Ogino, T. Minato, and M. Asada, “Visual attention by saliency leads cross-modal body representation,” in Proc. 7th Int. Conf. Develop. Learn. (ICDL), Shanghai, China, 2009.
S. M. Prabhu and D. P. Garg, “Artificial neural network based robot control: An overview,” J. Intell. Robot. Syst., vol. 15, pp. 333–365, 1996.
C. Gaskett and G. Cheng, “Online learning of a motor map for humanoid robot reaching,” in Proc. 2nd Int. Conf. Computat. Intell., Robot. Autonom. Syst. (CIRAS 2003), Singapore, 2003.

## Slide 24: Thank you!

## Slide 25: Discussion Piazza #1 Piazza @103_f5
To me, the most interesting part of this paper is the section on implicit representations. As this paper was written in 2010 just as deep learning was really starting to take off, the overall focus is still largely on models and hand-crafted systems with some learned components. I'd like to do more reading to see if there is some insight from biology that makes the CMAC specifically a good structure for motor control, or whether this is just similar to how CNNs are inspired by vision. Nowadays, it seems like the explosion in parameters and compute allows for the learning of much more complex implicit models (e.g. accurately predicting complex scene dynamics from images alone).

## Slide 26: Discussion Piazza #2 Piazza @103_f7
People can often estimate other's abilities for motions like parents can guess what their babies should be able to do and athletes can evaluate their opponents' physical capabilities or even read their intentions. So is it a valid research problem to discover if learning others' body representations. How should we formulate the problem?

## Slide 27: Discussion Class
Implicit model is generally preferred in today’s research community regarding robotic body representations since it offer more capacity for complex information storage and are able to adapt to changing scenarios.